## Slide 1: Synchronous Vs Asynchronous Reset
Reset
The signal used to initialize the hardware to a predefined sate
Synchronous reset
Reset samples with respect to the clock
Activates on the active clock edge when the reset signal is asserted
Asynchronous reset
Reset samples independent of the clock
Activates as soon as the reset signal is asserted.

## Slide 2: Active low asynchronous reset (Verilog code)
module d_flip_flop(q,d,clk,rst);
input d,clk,rst,rst;
output reg q;
always @(posedge clk or negedge rst)
begin
if(!rst)
q<=0;
else
q<=d;
end
endmodule

## Slide 3: Active low synchronous reset (Verilog code)
module d_flip_flop(q,d,clk,rst);
input d,clk,rst,rst;
output reg q;
always @(posedge clk)
begin
if(!rst)
q<=0;
else
q<=d;
end
endmodule